## Slide 1: CSG – EEG Toolbox
2016

## Slide 2: Installation
Installer SPM: http://www.fil.ion.ucl.ac.uk/spm/software/spm12/
2) ‘Fasst’ toolbox (see in the CSGtoolbox zip)
3) ‘CSG’ toolbox (see in the CSGtoolbox zip): has to be put on the top in the matlab set path.

## Slide 3: EEG preprocessing
Automatic preprocessing

## Slide 4: ‘CSG_preprocessing’
Preprocess your raw data via the ‘CSG_preprocessing’ function
New files are created:
1) the header and data files: .mat and .dat respectively
2) The filtered data: P_filename
3) Bad channels interpolated and detected: IP_filename

## Slide 5: ‘CSG_preprocessing’ Pipeline
Convert data to the SPM format
Clone data: Preprocessed data are saved under the name ‘P_initialdataname’
Filter data: EEG and other channels: [0.1-30]Hz, EOG channels: [0.1-5]Hz, EMG channels: [10-125]Hz.
Bad channels detection over large time-windows(‘CSG_badchannels’)
Interpolation of bad channels (‘CSG_interpol’)
Bad channels detected over small epochs (‘CSG_artefact’).
Three submethods are used to detect bad channels to check coherence:
between closed channels,
over small time-windows
over the whole recording
7) Rereferencing to the average of all channels

## Slide 6: EEG rereferencing
CSG toolbox

## Slide 7: ‘CSG_reref’ (256 channels)
You can rereference data to the average of the 256 channels:
- use the ‘CSG_reref’ function located in CSG/subfunction
- give in ‘origdir’ the path related to the toolbox ‘CSG’
- launch the function and select the ‘IP_filename’ file. It will return the file ‘MIP_filename’

## Slide 8: EEG display
CSG toolbox

## Slide 9: ‘CSG’

## Slide 10: Display

## Slide 11: Channels selection

## Slide 12: Interface
To go on specific channels (in red): either by selecting the channel or clicking on the map
To compute the spectrogram
To display events
To change the filtering
To choose:
the time window length
the number of channels to display
the scale
Save the current window for the next opening of this file

## Slide 13: EEG preprocessing
Manual Preprocessing

## Slide 14: Refine the preprocessed data
Display the EEG datafile preprocessed.
Click right on the EEG channel (s) you want to consider as cleaned or artefacted.

## Slide 15: Questions
If you have questions, you can ask to Jitka or me (by email)
Could you take notes of error messages or suggestions you have in order to improve the following beta version ;)
Thanks